## Slide 1: Computer Networks
IT4405

## Slide 2: Syllabus
Data Transmission Concepts
Packet Network Architecture
Internet Protocol Suit
Local Area Networks
Mobile Wide Area Networks
Network Design
Miscellaneous Concepts

## Slide 3: Data Transmission Concepts

## Slide 4: What is a Communication?
A process of Exchanging Information

## Slide 5: Transmission
Transmission is the process of sending, propagating and receiving an information signal (Analog / Digital) over a physical point to point or point to multipoint transmission medium either wired or wireless.

## Slide 6: Parallel Transmission
Sending multiple data parallel at a time is known as Parallel transmission.
Simply, Using ‘n’ wires to send ‘n’ bits at a time.
Diagram
Serial Transmission
In Serial transmission bits follow one another in one communication channel.
Simply, Using ‘1’ wire to send ‘n’ bits at a time.
Diagram

## Slide 7: Digital Signal
A continuous / smooth signal with infinite number of amplitude levels. OR
Continuous wave form in nature represented by continuous electromagnetic waves.
Graph
Analog Signal
A signal with limited number of levels.
Used in circuitry of a computer system.
Graph

## Slide 8: Transmission Medium
Data transmission Occurs between transmitter and receiver over some path which is known the transmission medium .
Classification Diagram.

## Slide 9: Unguided Media
Waves are guided along a physical path.
Copper or Optical
Guided Media
Wireless
Provide a means of transmitting electro magnetic wave, but do not guide them.
Propagation through air, vacuum and sea water.

## Slide 10: Transmission Impairments
With any communication system, the signal that is received may differ from the signal that is transmitted due to various transmission impairments.
For Analog Signals, - Signal quality is degraded.
For digital Signals, - Bit errors may be introduced that a binary 1 is transformed t binary 0 and vice versa.
1 – Attenuation
2 – Distortion
3 - Noise

## Slide 11: Attenuation
The loss of Signal strength with distance in any transmission medium.
Amplifiers and repeaters are used to regain / strengthen signals along the transmission path.
Diagram
dB = 10log10 (P2/P1) - P1, P2 are the powers of signal at points 1 and 2

## Slide 12: Example
A signal travels through a transmission medium and its power is reduced to half. What is the loss of power?
A signal travels through an amplifier and its power is increased 10 times. What is the gain of power?

## Slide 13: Distortion
Distortion means the signal change its form of shape.
This occurs in composite signals made of different frequencies.
Each component has its own propagation speed through a medium and therefore its own delay in arriving at final destination.
Diagram

## Slide 14: Noise
Noise is undesired and extra (additional unwanted) signals that are inserted somewhere between transmitter and receiver.
Diagram
Noise Types - Thermal Noise - Intermodulation Noise - Cross Talk - Impulse Noise

## Slide 15: CHANNEL CAPACITY
The maximum rate at which data can be transmitted over a given communication path, or channel, under given conditions, is referred to as the channel capacity.

## Slide 16
Data Rate The rate, in bits per second (bps), at which data can be communicated.
Bandwidth a range of frequencies within a given band, in particular that is used for transmitting a signal.
Error Rate The rate at which errors occur, where an error is the reception of a ‘1’ when a ‘0’ was transmitted or the reception of a ‘0’ when a ‘1’ was transmitted

## Slide 17
Noise The average level of noise over the communications path

## Slide 18: Nyquist Bit Rate
In the case of a channel that is noise free.
if the rate of signal transmission is 2B, then a signal with frequencies no greater than B is sufficient to carry the signal rate.
The converse is also true: Given a bandwidth of B, the highest signal rate that can be carried is 2B
If the signals to be transmitted are binary (two voltage levels), then the data rate that can be supported by B Hz is 2B bps

## Slide 19: Nyquist Formula
Bit Rate = 2 x Bandwidth x log2 L Where L is the number of signal levels.

## Slide 20: Example 01
Consider a noiseless channel with a bandwidth of 3000Hz transmitting a signal with two signal levels. What is the maximum bit rate?
Consider a same noiseless channel with a bandwidth of 3000Hz transmitting a signal with four signal levels. What is the maximum bit rate?

## Slide 21: Shannon Capacity Formula
Specifies the theoretical highest data rate of a channel
Capacity = Bandwidth x log2 (1 + SNR) - SNR : Signal to Noise Ratio

## Slide 22: Examples
A telephone line normally has a bandwidth of 3000Hz (300 Hz to 3300Hz). The SNR is usually 3162. What is the Capacity of this channel?